## Slide 1: Principles of Robot Autonomy I
Camera models and camera calibration

## Slide 2: Attendance Form

## Slide 3: Agenda
Agenda
  Perspective projections
  Camera calibration
  Basic concepts in 3D reconstruction
Readings:
  Chapter 7, sections 7.1 – 7.4 in D. Gammelli, J. Lorenzetti, K. Luo, G. Zardini, M. Pavone. Principles of Robot Autonomy. 2026.

## Slide 4: Perspective projection
Goal: find how world points map in the camera image
Assumption: pinhole camera model (all results also hold under thin lens model, assuming camera is focused at )
Roadmap:
  Map into p (image plane)
  Map p into (u,v) (pixel coordinates)
  Transform into
P in camera frame
P in world frame
World frame
Camera frame
Image plane
Notes: From now on we’ll focus on the pinhole camera model:
We will start by discussing today in details the geometry of the pinhole camera model. All the results derived using this camera model also hold for the thin lens model
As we discussed earlier, in the pinhole camera model, a point P in 3D (in the camera reference system) is mapped (projected) into a point P’ in the image plane.
This mapping or transformation is also referred to as Perspective projection.
The goal is to find how world points map in the camera image, that is how to map any 3D point from the 3D world directly into a point in pixel coordinates in the digital image.

## Slide 5: Step 1
  Task: Map into (image plane)
  From before
Notes: \tilde x = f\, \frac{X_C}{Y_C} + \tilde x_0, \qquad \tilde y = f\, \frac{Y_C}{Y_C} + \tilde y_0,

## Slide 6: Step 2.a
Actual origin of the camera coordinate system is usually at a corner (e.g., top left, bottom left)
Notes: The projection of 3D points into the image plane does not directly correspond to what we see in actual digital images (i.e., what we see in a display or monitor):
  i) points in the digital display are, in general, in a different reference system than those in the image/retinal plane;
  ii) Digital images are divided into pixels whereas points in the image/retina plane are measured in centimeters;
  iii) The physical sensors can introduce non-linearity (e.g. distortion) to the mapping.
Specifically, digital images typically have their origin at the lower-left corner of the image. Thus, 2D points in the image plane and 2D points in a digital image are equal up to an offset translation vector [x0 , y0 ],
\tilde x = f\, \frac{X_C}{Y_C} + \tilde x_0, \qquad \tilde y = f\, \frac{Y_C}{Y_C} + \tilde y_0,

## Slide 7: Step 2.b
Task: convert from image coordinates to pixel coordinates
Let and be the number of pixels per unit distance in image coordinates in the x and y directions, respectively
Nonlinear transformation
Notes: As second effect we need to take into account for is the fact that points in a digital image are expressed in pixels whereas points in the image plane are expressed in (e.g.) centimeters.
In order to accommodate this further change of coordinate systems, the mapping is now described by [..]
Notice that k_x is different from k_y because the aspect ratio of the unit element of the sensor (CCD or CMOS) is not necessarily 1 or the pixel aspect ratio is modified by the imaging system.
This is a non-linear transformation
It is easy to show that a linear transformation (mapping) can be always be expressed as a product of a matrix and the input signal [x y z]T . Is there a way we can express the projective equation as product of a matrix and the vector [X Y Z]?
u&= \alpha_u \frac{X_C}{Z_C} + u_0 \\
v&= \alpha_v \frac{Y_C}{Z_C} + v_0
u&= k_x \tilde x = k_x\, f\, \frac{X_C}{Z_C} + k_x \tilde x_0 \\
v&= k_y\tilde y = k_yf\, \frac{Y_C}{Z_C} + k_y\tilde y_0

## Slide 8: Homogeneous coordinates
Goal: represent the transformation as a linear mapping
Key idea: introduce homogeneous coordinates
Inhomogenous -> homogeneous
Homogenous -> inhomogeneous
Notes: One way to get around this problem is to change coordinate system and go from the Euclidean reference system (our original coordinate system) to the so called Homogenous coordinate system --- a new system of coordinates ubiquitous in projective geometry.
The process of going back and forth from Euclidean and Homogenous coordinate system is non-linear, but the good news is that once we are in the homogenous coordinate system a projective transformation becomes linear.
a point X in Rn (in the Euclidean coordinate system) is represented as Rn+1 vector (in the Homogenous coordinate system) by adding a final coordinate of 1.
A generic point X in Rn+1 (in the Homogenous coordinate system) is represented as a Rn vector (in the Euclidean coordinate system) by suppressing the last coordinate and dividing the first n coordinates of X by the n+1th coordinate.
The benefit of this will become clear in a second
\begin{pmatrix}
x\\
y
\end{pmatrix} \Rightarrow \begin{pmatrix}
x\\
y\\
1
\end{pmatrix} \qquad
\begin{pmatrix}
x\\
y\\
z
\end{pmatrix} \Rightarrow \begin{pmatrix}
x\\
y\\
z\\
1
\end{pmatrix}
\begin{pmatrix}
x\\
y
\end{pmatrix} \Rightarrow \begin{pmatrix}
x\\
y\\
1
\end{pmatrix} \qquad
\begin{pmatrix}
x\\
y\\
1
\end{pmatrix} \Rightarrow \begin{pmatrix}
x\\
y\\
z
\end{pmatrix}
\begin{pmatrix}
x\\
y\\
w
\end{pmatrix}\Rightarrow
\begin{pmatrix}
x/w\\
y/w
\end{pmatrix}
\qquad \begin{pmatrix}
x\\
y\\
z\\
w
\end{pmatrix}\Rightarrow \begin{pmatrix}
x/w\\
y/w\\
z/w
\end{pmatrix}

## Slide 9: Perspective projection in homogeneous coordinates
Projection can be equivalently written in homogeneous coordinates
In homogeneous coordinates, the mapping is linear:
in homogeneous coordinates
Homogeneous pixel coordinates
Camera matrix/
Matrix of intrinsic parameters
Point p in homogeneous pixel coordinates
Point in homogeneous camera coordinates
Notes: A point P=[x y z] in the 3D Euclidean reference system is expressed as Ph = [x y z 1] in Homogenous reference system. Let’s multiply the matrix K (which contains an arrangement of the camera parameters) by Ph: the result is a 3D vector, which converted to the Euclidean system is the desired point.
The conversion from Homogenous to Euclidean returns the actual point p (that’s where the non-linearity takes place).
This transformation is expressed as a multiplication of the matrix K and the vector Ph.
The projective transformation can be expressed as a linear transformation in the Homogenous reference system –
The key advantage of this representation is that we have obtained a much more compact expression for capturing the projective transformation.
P_c = \begin{pmatrix}
X_c\\
Y_c\\
Z_c
\end{pmatrix} \Rightarrow \begin{pmatrix}
X_c\\
Y_c\\
Z_c\\
1
\end{pmatrix} = P_c^h

## Slide 10: Skewness
In some (rare) cases
When is ?
  x- and y-axis of the camera are not perpendicular (unlikely)
  For example, as a result of taking an image of an image
Five parameters in total!
Skew parameter
Notes: We say that an image is skewed when the camera coordinate system is skewed; that is, the two image axes are not perpendicular (as they should) and the angle θ between the two axes is slightly larger or smaller than 90 degrees.
5 parameters: These parameters encompass focal length, image sensor format, and principal point.
K = \begin{bmatrix}
\alpha &{\color{red} \gamma} & u_0\\
0 & \beta & v_0\\
0 & 0& 1
\end{bmatrix}

## Slide 11: Step 3
So far, we have derived a mapping between a point P in the 3D camera reference frame to a point p in the 2D image plane
Last step is to include in our mapping an additional transformation to account for the difference between the world frame and the 3D camera reference frame
Notes: So we far we have described a mapping between a point P in the 3D camera reference system to a point p in the 2D image plane. But what if the information we have about points in 3D (or in general about any physical object) is available in the world coordinate system?
Then, we need to include to our mapping an additional transformation that allows to relate points from/to the world reference system to/from the camera reference system. This transformation is captured by a rotation matrix R and a translation vector T.

## Slide 12: Rigid transformations
where R is the rotation matrix relating camera and world frames
Notes:   The transformation that allows to relate points from/to the world reference system to/ from the camera reference system is a rigid transformation and is regulated by a translation t and a rotation R in 3D.
\Rightarrow P_C = t+ R\, P_W
R = \begin{bmatrix}
i_W\cdot i & j_W\cdot i & k_W\cdot i\\
i_W\cdot j & j_W\cdot j & k_W\cdot j\\
i_W\cdot k & j_W\cdot k & k_W\cdot k\\
\end{bmatrix}

## Slide 13: Rigid transformations in homogeneous coordinates
Point in homogeneous coordinates
Point in homogeneous coordinates
Notes: The benefit of working in a homogeneous coordinates is that these two transforma6ons can be compactly described by the matrix [R T; O 1] as the slide illustrates.
This is a 4x4 matrix and allows to map any point Pw = [xw yw zw 1]T in the world reference system to a point P = [x y z 1]T in the camera reference system (in homogenous coordinates)
\begin{pmatrix}
P_C\\
1
\end{pmatrix}
= \begin{bmatrix}
R & t\\
0_{1\times 3} & 1
\end{bmatrix}\begin{pmatrix}
P_W\\
1
\end{pmatrix}

## Slide 14: Perspective projection equation
Collecting all results
Hence
Degrees of freedom: 4 for K (or 5 if we also include skewness), 3 for R, and 3 for t. Total is 10 (or 11 if we include skewness)
Intrinsic parameters
Extrinsic parameters
Projection matrix M
Notes: The projection mapping is compactly given by the projectiion matrix K [R T], where K are called internal or intrinsic parameter and [R T] are called the external or extrinsic parameters
The former are related to the intrinsic physical properties of the camera (e.g. focal length, etc…) where the latter are related to pose and location of the camera;
Notice that these two set of parameters are nicely separated in this formulation.
p^h = [K \quad 0_{3\times 1}]P_C^h = K[I_{3\times 3} \quad 0_{3\times 1}]\begin{bmatrix}
R & t\\
0_{1\times 3} & 1
\end{bmatrix}P_W^h

## Slide 15: Camera calibration: direct linear transformation method
Goal: find the intrinsic and extrinsic parameters of the camera
Strategy: given known correspondences , compute unknown parameters K, R, t by applying perspective projection
with known positions in world frame
with known positions in image frame
Credit: FP Chapter 1
Notes: Recall that our camera is modeled using internal, or intrinsic, parameters (K) and external, or extrinsic, parameters ([R T]). Their product gives us the full 3x4 projection matrix, shown before. It has 11 degrees of freedom
Problem: given one or more images taken by a camera, estimate its intrinsic and extrinsic parameters.
We can describe this problem more precisely using a calibration rig, such as the one shown above.
The rig usually consists of a pattern (usually a checkerboard) with known dimensions. The rig also defines our world reference coordinate frame ([Ow,iw,jw,kw] as shown in the figure.
Now, suppose we are given n points on the calibration rig, P1 … Pn , along with their corresponding coordinates, p1 , … pn in the image. Using these correspondences, our goal is to estimate both intrinsic and extrinsic parameters.

## Slide 16: Step 1
First consider combined parameters
This gives rise to component-wise equations, for
vector
Notes: In the next slides, we will set up a linear system of equations from n of such correspondences and propose a procedure for solving it against the unknowns (intrinsic and extrinsic parameters).
Let’s consider the ith correspondence pair defined by a point Pi in the calibration rig (in the world reference system) and its observation pi in the image [….]
This gives rise to component-wise equations
u_i\, (m_3\cdot P_{W,i}^h) - m_1\cdot{P_{W,i}^h}=0\\
v_i\, (m_3\cdot P_{W,i}^h) - m_2\cdot{P_{W,i}^h}=0
u_i &= \frac{m_1\cdot{P_{W,i}^h}}{m_3\cdot{P_{W,i}^h}}\\
v_i &= \frac{m_2\cdot{P_{W,i}^h}}{m_3\cdot{P_{W,i}^h}}
p^{h}_i = M \, P_{W,i}^h, \, \, i=1,\ldots, n, \qquad \text{where} \quad M = K[R \quad t] = \begin{bmatrix}
m_1\\
m_2\\
m_3\end{bmatrix}
In the next slides, we will set up a linear system of equations from n of such correspondences and propose a procedure for solving it against the unknowns (intrinsic and extrinsic parameters).
Let’s consider the ith correspondence pair defined by a point Pi in the calibration rig (in the world reference system) and its observation pi in the image [….]
This gives rise to 2𝑛 component-wise equations
u_i\, (m_3\cdot P_{W,i}^h) - m_1\cdot{P_{W,i}^h}=0\\
v_i\, (m_3\cdot P_{W,i}^h) - m_2\cdot{P_{W,i}^h}=0
u_i &= \frac{m_1\cdot{P_{W,i}^h}}{m_3\cdot{P_{W,i}^h}}\\
v_i &= \frac{m_2\cdot{P_{W,i}^h}}{m_3\cdot{P_{W,i}^h}}
p^{h}_i = M \, P_{W,i}^h, \, \, i=1,\ldots, n, \qquad \text{where} \quad M = K[R \quad t] = \begin{bmatrix}
m_1\\
m_2\\
m_3\end{bmatrix}

## Slide 17: Calibration problem
Stacking all equations together
contains in block form the known coefficients stemming from the given correspondences
To estimate 11 coefficients, we need at least 6 correspondences
12 x 1
12 x 1 vector of unknown coefficients
2n x 12 matrix of known coefficients
Notes: We can express these contraints it in terms of a matrix equation of the form Pm = 0
Note that m is a vectorized version of the 3x4 projection matrix, where each 4x1 block corresponds to a row in the original matrix.
0 is always a solution. Furthermore, if m is a solution, then so is k m, where k is an arbitrary scaling factor.
P m =0, \qquad \text{where } m = \begin{bmatrix}m_1^T\\m_2^T \\m_3^T \end{bmatrix}

## Slide 18: Solution
To find non-zero solution
Solution: select eigenvector of with the smallest eigenvalue
Readily computed via SVD (singular value decomposition)
Notes: When 2n>11, the homogeneous linear system is overdetermined.
0 is always a solution. Furthermore, if m is a solution, then so is k m, where k is an arbitrary scaling factor.
Here we are interested in finding a non-zero vector in the nullspace of M . Since the scale is arbitrary we can add the constraint kvk2 = 1 In most cases the system Mv = 0 will not have any exact solution due to noise in the measurements. Therefore we will search for a solution to […]
Therefore, to constrain our optimization, we minimize |P m|2 subject to the constraint that |m|2 = 1
We can obtain the least-squares solution for m by factorizing P to UDVT using SVD and then taking the last column of V.
\underset{m\in R^{12}}{\text{min}} \quad & \| \tilde P m\|^2\\
\text{subject to}\quad & \| m\|^2 = 1

## Slide 19: Step 2
Next, we need to extract the camera parameters, i.e., we want to factorize M as
This can be done efficiently (indeed, explicitly) by using RQ factorization, whereby the submatrix is decomposed into the product of an upper triangular matrix K and a rotation matrix R
These concepts will be investigated further in Problem 1 in HW3
Notes: Once we have estimated the combined parameters in m, the next step is to extract the actual intrinsics and extrinsics from it.
If A is an n n matrix then there is an orthogonal matrix Q and a right triangular matrix R such that A = RQ:
\tilde P = [KR\quad Kt]

## Slide 20: Measuring depth
Homogeneous coordinates
Once the camera is calibrated, can we measure the location of a point P in 3D given its known observation p?
  No: one can only say that P is located somewhere along the line joining p and O!
Line of sight
Notes: it is in general not possible to recover the structure of the 3D world from just one image. This is due to the intrinsic ambiguity of the 3D to 2D mapping.
Any point along the ray from the camera center O to a point p in the image (line of sight) is a possible candidate for the actual 3D point P.

## Slide 21: Issues with recovering structure
Notes: As we can see in this image, it is easy to fool our eyes. The pisa tower here is much further that the shoe of this person even if it looks like this person is kicking the tower!
By careful inspection we could actually use the ground plane and the location of the object’s base as cues, and can figure out that the tower is actually in the background and that the person is in the foreground.
If we use two eyes, or move our head a little bit, this illusion immediately disappears and we can perfectly figure out the correct scene layout.

## Slide 22: Recovering structure
Structure: 3D scene to be reconstructed by having access to 2D images
Common methods
  Through recognition of landmarks (e.g., orthogonal walls)
  Depth from focus: determines distance to one point by taking multiple images with better and better focus
  Stereo vision: processes two distinct images taken at the same time and assumes that the relative pose between the two cameras is known
  Structure from motion: processes two images taken with the same or different cameras at different times and from different unknown positions
Notes: Four methods are possible

## Slide 23: Stereopsis, or why we have two eyes
Notes: What if there are two cameras observing the object?
Fusing the pictures recorded by our two eyes and exploiting the difference (or disparity) between them allows us to gain a strong sense of depth.
We now focus on the design and implementation of algorithms that mimic our ability to perform this task, known as stereopsis .

## Slide 24: Binocular reconstruction
Given: calibrated stereo rig and two image matching points and
Find corresponding scene point by intersecting the two rays and (process known as triangulation)
Notes: Here’s how having two eyes (or alternately, cameras) help. Suppose we have two cameras with known camera intrinsic parameters K and K’, respectively, and known relative locations and orientations (i.e., we know the transformations R and T that relate the two camera reference systems).
Suppose we have a point P in 3D. Let p and p’ be the observations of P in the images of camera 1 and 2, respectively.
The location of P is unknown in the 3D space, but we can measure the locations of p and p’ in each image. Because K, K’, R and T are known, we can compute the two lines of sight l and l’ which are defined by O and p, and O’ and p’, respectively.
Thus, P can be computed as the intersection point between l and l’.
This process is known as Triangulation.
\begin{cases}
p^h \times M \, P^h = 0\\
p^{h,\prime} \times M \, P^{h,\prime} = 0
\end{cases}

## Slide 25: Approximate triangulation
Due to noise, triangulation problem is often solved as finding the point Q with images and that minimizes
Re-projection error
Notes: In practice, because the observations p and p’ are noisy and the camera calibration parameters may not be accurately estimated, finding the intersection point P may be problematic (in fact, the exact intersection point may not exist at all).
Thus, the triangulation problem is often mathematically characterized by solving the minimization problem where we optimize the reprojection error, that is
we seek to find a point Q in 3D that best approximates P by minimizing the re-projection error of Q in both images.
d^2(p,q) + d^2(p^{\prime}, q^{\prime})

## Slide 26: Next time: image processing, feature detection & description
Notes: Structure from motion (SfM) is a photogrammetric range imaging technique for estimating three-dimensional structures from two-dimensional image sequences that may be coupled with local motion signals.
Optical flow or optic flow is the pattern of apparent motion of objects, surfaces, and edges in a visual scene caused by the relative motion between an observer and a scene