## Slide 1: Principles of Robot Autonomy I
State space dynamics – definitions and modeling

## Slide 2: Attendance Form

## Slide 3: For urgent questions
aa174a-aut2526-staff@lists.stanford.edu
Please do not email Prof. Pavone or the CAs individually unless there is a specific reason!

## Slide 4: Agenda
State space dynamics
  Definitions
  Modeling (kinematic and dynamic models)
  Special case: LTI systems and linearization
Readings
  Chapter 1, sections 1.1 – 1.3 in D. Gammelli, J. Lorenzetti, K. Luo, G. Zardini, M. Pavone. Principles of Robot Autonomy. 2026.

## Slide 5: State space models
We can control a robot through the inputs to the system (e.g., motor torques, rotor thrusts, etc.)
The state of a robot is a collection of variables (e.g., position, velocity) that change over time in response to the inputs
A state space model is a mathematical description of how the state evolves over time (i.e., or ) in response to the inputs
Notes: The state x(t_0) of the system at time t_0 is the information at t_0 that, together with the input u(t) for t\geq t_0, determines uniquely the output y(t) for all t\geq t_0

## Slide 6: Example: double-integrator
Suppose we can control the force pushing on a cart
Newton’s second law tells us that
Let with , and . Then we can write
Notes: This is an example of a dynamic models

## Slide 7: Kinematic models
Kinematic models are mathematical models that describe the motion of a system without consideration of forces
Kinematic models typically result from geometric constraints on the motion of a system, before considering any forces
For example, the “unicycle” with generalized coordinates should not slip sideways, i.e.,
This relation induces a kinematic model, as we will see shortly
Notes: From the definitions above, kinematics describe constraints that arise from the robot’s physical state or geometry, whereas dynamics explain how forces or inputs influence the robot’s motion.
To derive such models, we need to introduce the notions of configuration and generalized coordinates. A robot’s physical state, also referred to as its configuration, provides a complete specification of the position of every point on the robot at a given instant.
A configuration can be represented using a set of variables known as generalized coordinates, denoted by q(t)
Consider a disk that rolls without slipping on the horizontal plane, while keeping its sagittal plane (i.e., the plane that contains the disk) in the vertical direction
This system, referred as a unicycle, is described by three DOF
No side slip (pure rolling) constraint: entails that the velocity of the contact point has zero component in the direction orthogonal to the sagittal plane

## Slide 8: Holonomic and nonholonomic constraints
More broadly, constraints on degrees of freedom come in various forms: Pfaffian constraints are a special, yet common case of nonholonomic constraints
If has rows (constraints) and columns (DOFs), then where is a basis for admissible velocities, i.e., the null space of .
Kinematic model of the constrained system
Notes: Holonomic constraints are constraints that can be expressed in the form of equality constraints involving only the generalized coordinates q, .
The effect of holonomic constraints is to reduce the space of accessible configurations to a subset with dimension n − k, assuming we have k constraints
Holonomic constraints are generally the result of mechanical interconnections between the various bodies of the system. For example, prismatic and revolute joints used in robot manipulators are a typical source of such constraints, and joint variables are an example of reduced sets of coordinates.
As a concrete example, consider a pendulum, or a revolute joint determines two holonomic constraints: while six parameters are necessary to define the configuration of two free-flying planar robots, four parameters suffice to determine the position and orientation
Loosely, non-holonomic constraints involve generalized coordinates and their velocities
Nonholonomic constraints reduce mobility in a completely different way.
If the constraints are holonomic, there is a loss of accessibility, as the motion of the mechanical system in C is confined to a particular level surface of the scalar function h
Assume instead that the constraint is nonholonomic. In this case, generalized velocities are indeed constrained to belong to the null space of the constraint matrix.
Assume the motion of a system is subject to k Pfaffian constraints
Then, the admissible velocities at each configuration belong to the (d − k)-dimensional null space of matrix G
Denoting by a basis of the null space of G, admissible trajectories can be characterized as solutions to
%
More precisely, an matrix M represents a linear map where is the underlying field.[5] So, the dimension of the domain of is n, the number of columns of M, and the rank–nullity theorem for an matrix M is
rank(M) + nullity (M) = n
Holonomic constraints are constraints that can be expressed in the form of equality constraints involving only the generalized coordinates q, .
The effect of holonomic constraints is to reduce the space of accessible configurations to a subset with dimension n − k, assuming we have k constraints
Holonomic constraints are generally the result of mechanical interconnections between the various bodies of the system. For example, prismatic and revolute joints used in robot manipulators are a typical source of such constraints, and joint variables are an example of reduced sets of coordinates.
As a concrete example, a revolute joint determines two holonomic constraints: while six parameters are necessary to define the configuration of two free-flying planar robots, four parameters suffice to determine the position and orientation
Loosely, non-holonomic constraints involve generalized coordinates and their velocities
Nonholonomic constraints reduce mobility in a completely different way.
If the constraints are holonomic, there is a loss of accessibility, as the motion of the mechanical system in C is confined to a particular level surface of the scalar function h
Assume instead that the constraint is nonholonomic. In this case, generalized velocities are indeed constrained to belong to the null space of the constraint matrix.
Assume the motion of a system is subject to k Pfaffian constraints
Then, the admissible velocities at each configuration 𝑞 belong to the (d − k)-dimensional null space of matrix G(𝑞)
Denoting by \{𝑔_1 𝑞, …,𝑔_(𝑛−𝑑) (𝑞)\} a basis of the null space of Gq𝜉), admissible trajectories can be characterized as solutions to

## Slide 9: Back to unicycle example
The “unicycle” with DOFs should not slip sideways, i.e.,
Physically, is the forward velocity of the wheel, and is its rotational steering velocity
Notes: All admissible velocities are therefore obtained as linear combination of and
The null space in this case is spanned by the vectors [cosθ, sinθ, 0] and [0, 0, 1] which suggests that any potential motion must be made up of a linear combination of these vectors. Intuitively this would be expected because [cos θ, sin θ, 0] is the unit vector in the direction of rolling, and [0, 0, 1] would correspond to the wheel spinning but not rolling.
The constraint is non-holonomic because it implies no loss of accessibility in the configuration space of the disk. -> simple 3-step motion
All admissible velocities are therefore obtained as linear combination of 𝑔_1 (𝜉) and 𝑔_2 (𝜉)
The null space in this case is spanned by the vectors [cosθ, sinθ, 0] and [0, 0, 1] which suggests that any potential motion must be made up of a linear combination of these vectors. Intuitively this would be expected because [cos θ, sin θ, 0] is the unit vector in the direction of rolling, and [0, 0, 1] would correspond to the wheel spinning but not rolling.
The constraint is non-holonomic because it implies no loss of accessibility in the configuration space of the disk. -> simple 3-step motion

## Slide 10: Unicycle and differential drive models
unicycle
differential drive
We can alternate between these kinematic models via the one-to-one input mappings:
Notes: For example, in the case of the unicycle, one obtains the model..
For the unicyle the inputs v and ω have a clear physical interpretation. In particular,
  v is the driving velocity, that is the i.e., the modulus (with sign) of the contact point velocity vector
  whereas the steering velocity ω is the wheel angular speed around the vertical axis. Note that they are independent!
Note: the choice of the input vector fields is not unique. Correspondingly, the components of the inputs may have different meanings
A unicycle in the strict sense (i.e., a vehicle equipped with a single wheel) is a robot with a serious problem of balance in static conditions. However, there exist vehicles that are kinematically equivalent to a unicycle but more stable from a mechanical viewpoint.
The differential drive model is a variation on the unicycle model from the previous section, with two wheels fixed on a shared rear axle and a passive front wheel that induces no additional kinematic constraints
Among these, the most important is the differential drive robot. One can show that the kinematic model of the unicycle also applies to the differential drive vehicle, provided that the driving and steering velocities v and ω are expressed as a function of the the angular speeds of the right and left wheels, ωR and ωL , respectively.
%%%%%%%%
  If the wheels are rotating on ground (i.e. there is no slipping), then there is a point ICC
  While we can vary the velocity of each wheel, for the robot to perform rolling motion, the robot must rotate about a point that lies along their common left and right wheel axis. The point that the robot rotates about is known as the ICC - Instantaneous Center of Curvature
  By using omega = rv, one obtains te relations
Another important model is the bicycle model, which is four-dimensional
Kinematically equivalent vehicles that are mechanically balanced the tricycle and the car-like robot
We’ll go deeper on this in the pset for the differential drive
|u_1|&\leq u_{1,{\text{max}}}\\
|u_2|&\leq u_{2,{\text{max}}}\\
|\zeta| &\leq \zeta_{\text{max}}
|v|&\leq v_{\text{max}}\\
|\omega| &\leq \omega_{\text{max}}
\begin{pmatrix}
\dot x\\
\dot y\\
\dot \theta\\
\dot \zeta
\end{pmatrix} = \begin{pmatrix}
\cos \zeta \, \cos\theta\\
\cos\zeta \, \sin \theta\\
\sin \zeta\\
0
\end{pmatrix} u_1 + \begin{pmatrix}
0\\
0\\
0\\
1
\end{pmatrix}u_2
\begin{pmatrix}
\dot x\\
\dot y\\
\dot \theta
\end{pmatrix} = \begin{pmatrix}
\cos\theta\\
\sin \theta\\
0
\end{pmatrix} v + \begin{pmatrix}
0\\
0\\
1
\end{pmatrix}\omega
\begin{pmatrix}
\dot x\\
\dot y\\
\dot \theta
\end{pmatrix} = \begin{pmatrix}
\frac{r}{2}(\omega_l + \omega_r)\cos\theta\\
\frac{r}{2}(\omega_l + \omega_r)\sin\theta\\
\frac{r}{L}(\omega_r-\omega_l)
\end{pmatrix}\
|\omega_l|\leq \omega_{l,\mathrm{max}}\\
|\omega_r|\leq \omega_{r,\mathrm{max}}
v = \frac{r(\omega_r + \omega_l)}{2}

## Slide 11: Simple car model
References:
J.-P. Laumond. Robot motion planning and control. 1998.
S. LaValle. Planning algorithms. 2006.
Simple car model
Reeds-Shepp car
Dubins car
states:
inputs:
Notes: Another important model is the siplified car model,
|u_1|&\leq u_{1,{\text{max}}}\\
|u_2|&\leq u_{2,{\text{max}}}\\
|\zeta| &\leq \zeta_{\text{max}}
|v|&\leq v_{\text{max}}\\
|\omega| &\leq \omega_{\text{max}}
\begin{pmatrix}
\dot x\\
\dot y\\
\dot \theta\\
\dot \zeta
\end{pmatrix} = \begin{pmatrix}
\cos \zeta \, \cos\theta\\
\cos\zeta \, \sin \theta\\
\sin \zeta\\
0
\end{pmatrix} u_1 + \begin{pmatrix}
0\\
0\\
0\\
1
\end{pmatrix}u_2
\begin{pmatrix}
\dot x\\
\dot y\\
\dot \theta
\end{pmatrix} = \begin{pmatrix}
\cos\theta\\
\sin \theta\\
0
\end{pmatrix} v + \begin{pmatrix}
0\\
0\\
1
\end{pmatrix}\omega
|v = v_{\mathrm{max}}, \, \, |\phi|\leq \phi_{\mathrm{max}}<\frac{\pi}{2}

## Slide 12: From kinematic to dynamic models
A kinematic state space model should be interpreted only as a subsystem of a more general dynamical model
Improvements to the previous kinematic models can be made by placing integrators in front of action variables
For example, for the unicycle model, one can set the speed as the integration of an action representing acceleration, that is
states: inputs:
Notes: Warning: a kinematic state space model should be interpreted only as a subsystem of a more general dynamical model
In almost all applications, a black-box module allows to control directly the linear and angular velocities of the mobile robot. Velocities and accelerations are of course submitted to bounds. This process allows to go from kineamtically feasible paths to dynamically feasible trajectories. One could also reason in terms of dynamical models
We’ll go deeper on this in the pset for the differential drive

## Slide 13: Linear time-invariant models
In general, is nonlinear, which can make it difficult to analyze
Linear time-invariant (LTI) models take the form with constant matrices and
For with , the solution is . If , the system is stable, i.e., converges to zero over time
For with , the solution is , where is the matrix exponential
Analogously to the scalar case, if for each eigenvalue of , then the system is stable
Notes: Scalar case is like a 1x1 matrix, and so the scalar is an eigenvalue of itself.
Without going into details on Jordan normal forms, etc., we can say the matrix exponential is always a sum of possibly time-varying coefficient matrices, each multiplied by an exponential term.
Critically, the terms of these coefficient matrices C(t) are always either sinusoids or powers of “t”, so the scalar exponential factor determines the prevailing growth/decay rate of each term.

## Slide 14: Example: PD control for a double-integrator
Let with , and . Then
Choose . Then with eigenvalues . If and , then for each eigenvalue , so the cart converges to a stand-still at
This is nice, can we use linear control tools if the system is non-linear?
Notes: Derivative acts as a brake or dampener on the control effort.
The proportional term looks at where my value is currently. Derivative tries to work opposite of where proportional is trying to drive the process. P is trying to drive one way, and D is trying to counteract that.
Increasing the proportional gain () has the effect of proportionally increasing the control signal for the same level of error. The fact that the controller will "push" harder for a given level of error tends to cause the closed-loop system to react more quickly, but also to overshoot more. Another effect of increasing is that it tends to reduce, but not eliminate, the steady-state error
The addition of a derivative term to the controller () adds the ability of the controller to "anticipate" error. With simple proportional control, if is fixed, the only way that the control will increase is if the error increases. With derivative control, the control signal can become large if the error begins sloping upward, even while the magnitude of the error is still relatively small. This anticipation tends to add damping to the system, thereby decreasing overshoot. The addition of a derivative term, however, has no effect on the steady-state error.
%%
Increasing the proportional gain () has the effect of proportionally increasing the control signal for the same level of error. The fact that the controller will "push" harder for a given level of error tends to cause the closed-loop system to react more quickly, but also to overshoot more. Another effect of increasing is that it tends to reduce, but not eliminate, the steady-state error.
The addition of a derivative term to the controller () adds the ability of the controller to "anticipate" error. With simple proportional control, if is fixed, the only way that the control will increase is if the error increases. With derivative control, the control signal can become large if the error begins sloping upward, even while the magnitude of the error is still relatively small. This anticipation tends to add damping to the system, thereby decreasing overshoot. The addition of a derivative term, however, has no effect on the steady-state error.
The addition of an integral term to the controller () tends to help reduce steady-state error. If there is a persistent, steady error, the integrator builds and builds, thereby increasing the control signal and driving the error down. A drawback of the integral term, however, is that it can make the system more sluggish (and oscillatory) since when the error signal changes sign, it may take a while for the integrator to "unwind.”
The proportional term looks at where my value is currently. Integral looks at where I’ve been over time, and derivative tries to predict where I’m going. Derivative tries to work opposite of where proportional and integral are trying to drive the process. P and I are trying to drive one way, and D is trying to counteract that. Derivative has its largest effect when the process is changing rapidly in one direction. The P and I terms are saying, ‘Keep going.’ The derivative catches it and says, ‘You’re going too fast. You need to slow down

## Slide 15: Linearization
slope
delta
offset
Linearization approximates a nonlinear function near by a line, i.e., linear function
The “slope” of the line is the derivative of at . The change in near is the slope multiplied by the distance from
The quality of the approximation can vary with the linearization point and distance from

## Slide 16: Linearization of non-linear state-space models
For the nonlinear system , the linearization around is Since and can be vectors, we generalize derivatives to Jacobian matrices
If is an equilibrium, i.e., we can consider an LTI approximation of the system near , with state and input
When is near , we can use tools from linear systems analysis and control on nonlinear systems -- more on this later with LQR control!
Notes: the Jacobian of a vector-valued function of several variables is the matrix of all its first-order partial derivatives.
Suppose f : Rn → Rm is a function such that each of its first-order partial derivatives exist on Rn.
Then the Jacobian matrix of f is defined to be an m×n matrix, denoted by J, whose (i,j)th entry is
{\textstyle \mathbf {J} _{ij}={\frac {\partial f_{i}}{\partial x_{j}}}}, or explicitly

## Slide 17: Example: Inverted pendulum
The dynamics are described by . In state space form with , they are
Since is an equilibrium, the linearization here is
This is close to a double-integrator! We could try to stabilize the pendulum near the upright equilibrium
Notes: The net torque of the system must equal the moment of inertia times the angular acceleration:

## Slide 18: Example: Inverted pendulum
We try to stabilize the pendulum near the upright equilibrium:
We will later discuss how we actually simulate this system on a computer

## Slide 19: Next time

## Slide 20: Attendance Form