## Slide 1: Principles of Robot Autonomy I
Motion planning I: graph search algorithms

## Slide 2: Attendance Form

## Slide 4: Agenda
Agenda
  Introduction to motion planning
  Search-based algorithms for motion planning
  Configuration spaces and combinatorial motion planning
Readings:
  Chapter 4, sections 4.1 – 4.2 in D. Gammelli, J. Lorenzetti, K. Luo, G. Zardini, M. Pavone. Principles of Robot Autonomy. 2026.

## Slide 5: Motion planning
Problem definition: Compute sequence of actions that drives a robot from an initial condition to a terminal condition while avoiding obstacles, respecting motion constraints, and possibly optimizing a cost function

## Slide 6: The see-think-act cycle
Notes: Going back to the question on how to make a robot autonomous, a typical paradigm is represented by the see-think-act cycle
Where am I, what should I do, and do it
Four steps
Division is artificial, some steps could be blended

## Slide 8: More examples of motion planning
Steering autonomous vehicles
Controlling humanoid robot
Surgery planning
Protein folding
…

## Slide 9: Some history
Formally defined in the 1970s
Development of exact, combinatorial solutions in the 1980s
Development of sampling-based methods in the 1990s
Deployment on real-time systems in the 2000s
Current research: inclusion of differential and logical constraints, planning under uncertainty, parallel implementation, and more

## Slide 10: Simplest setup
Assume 2D workspace:
is the obstacle region with polygonal boundary
Robot is a rigid polygon
Problem: given initial placement of robot, compute how to gradually move it into a desired goal placement so that it never touches the obstacle region

## Slide 11: Popular approaches
Potential fields [Rimon, Koditschek, '92]: create forces on the robot that pull it toward the goal and push it away from obstacles
Grid-based planning [Stentz, '94]: discretizes problem into grid and runs a graph-search algorithm (Dijkstra, A*, …)
Combinatorial planning [LaValle, '06]: constructs structures in the configuration (C-) space that completely capture all information needed for planning
Sampling-based planning [Kavraki et al, '96; LaValle, Kuffner, '06, etc.]: uses collision detection algorithms to probe and incrementally search the C-space for a solution, rather than completely characterizing all of the structure

## Slide 12: Grid-based approaches
Discretize the continuous world into a grid
  Each grid cell is either free or forbidden
  Robot moves between adjacent free cells
  Goal: find sequence of free cells from start to goal
Mathematically, this corresponds to pathfinding in a discrete graph
  Each vertex represents a free cell
  Edges connect adjacent grid cells

## Slide 13: Graph search algorithms
Having determined decomposition, how to find “best” path?
Label-Correcting Algorithms: : cost-of-arrival from
FRONTIER/ALIVE/PRIORITY QUEUE
Node
Nodes
Yes
Notes: The idea is to progressively discover shortest paths from the origin to every node i and to maintain the length of the shortest path found so far in a variable C called the label
Frontier list contains info about active nodes
One can show by induction that C is either infinity, or represent the length of some path to q
Path can be constructed by backward tracing

## Slide 14: Label correcting algorithm
Step 1. Remove a node from frontier queue and for each child of , execute step 2
Step 2. If , set and set to be the parent of . In addition, if, place in the frontier queue if it is not already there, while if , set UPPER to the new value
Step 3. If the frontier queue is empty, terminate, else go to step 1
Initialization: set the labels of all nodes to , except for the label of the origin node, which is set to 0

## Slide 15: GetNext() ?
Depth-First-Search (DFS): Maintain as a stack – Last in/first out
Lower memory requirement (only need to store part of graph)
Breadth-First-Search (BFS, Bellman-Ford): Maintain as a list – First in/first first out
Update cost for all edges up to current depth before proceeding to greater depth
Can deal with negative edge (transition) costs
Best-First (BF, Dijkstra): Greedily select next q:
Node will enter the frontier queue at most once
Requires costs to be non-negative
Notes: There is cosiderable freedom in selecting the node that can be remove from the frontier list at each step
DFS for tree graph: at the time the node marked exits, only the solid line portion of the tree is needed in memory

## Slide 16: Correctness and improvements
If a feasible path exists from to , then algorithm terminates in finite time with equal to the optimal cost of traversal, .
Theorem
* https://en.wikipedia.org/wiki/Dijkstra%27s_algorithm
Notes: Explores options in every “direction” § No information about goal location

## Slide 17: A*: Improving Dijkstra
Dijkstra orders by optimal “cost-to-arrival”
Faster results if order by “cost-to-arrival”+ (approximate) “cost-to-go”
That is, strengthen test
to
where is a heuristic for optimal cost-to-go (specifically, a positive underestimate)
In this way, fewer nodes will be placed in the frontier queue
This modification still guarantees that the algorithm will terminate with a shortest path
Many variations are possible… see (Problem 2 in pset 2)
Notes: Dijkstra's algorithm, as another example of a uniform-cost search algorithm, can be viewed as a special case of A* where {\displaystyle h(x)=0} for all x

## Slide 18: Grid-based approaches: summary
Pros:
  Simple and easy to use
  Fast (for some problems)
Cons:
  Resolution dependent
    Not guaranteed to find solution if grid resolution is not small enough
  Limited to simple robots
    Grid size is exponential in the number of DOFs

## Slide 19: Back to continuous motion planning
Assume 2D workspace:
is the obstacle region with polygonal boundary
Robot is a rigid polygon
Problem: Given initial placement of robot, compute how to gradually move it into a desired goal placement so that it never touches the obstacle region

## Slide 20: Back to continuous motion planning
Key point: motion planning problem described in the real-world, but it really lives in another space -- the configuration (C-) space!

## Slide 21: Configuration space
C- space: captures all degrees of freedom (all rigid body transformations)
More in detail, let be a polygonal robot (e.g., a triangle)
The robot can rotate by angle or translate
Every combination yields a unique robot placement: configuration
So C- space is a subset of
Note: yields equivalent rotations C- space is:
Concept of C- space extends naturally to higher dimensions (e.g., robot linkages)

## Slide 22: Configuration free space
The subset of all collision free configurations is the free space
obstacle
forbidden space
free space

## Slide 24
Bottom line: explicitly computing C free spaces in high-dimensional settings is hard!

## Slide 25: Planning in C-space
Let denote set of points in the world occupied by robot when in configuration
Robot in collision
Accordingly, free space is defined as:
Path planning problem in C-space: compute a continuous path: , with and

## Slide 26: Combinatorial planning
Combinatorial approaches to motion planning find paths through continuous configuration space without resorting to approximations
Key idea: compute a roadmap, which provides a discrete representation of continuous motion planning problem without losing any of the original connectivity information needed to solve it
Such approaches are typically complete (i.e., guaranteed to find a solution), but are typically limited to small number of DOFs due to the challenge of exactly computing C free spaces
A roadmap is a graph in which each vertex is a configuration in and each edge is a path through that connects a pair of vertices
Notes: Check connectivity combinatorial

## Slide 27: Next time: sampling-based planning