## Slide 1: AA203 Optimal and Learning-based Control
HJB, HJI, and reachability analysis
Notes: Anitcipative sreategies
Check skide 8
Change gamma
Fix slide 20

## Slide 2: Roadmap
Open-loop
Indirect methods
Direct
methods
Closed-loop
DP
HJB / HJI
MPC
Adaptive
optimal control
Model-based RL
Model-free RL
Control
Optimal and learning control
Adaptive control
Feedback control
LQR
iLQR
DDP
2
Reachability analysis
LQR

## Slide 3: Dynamic Programming
Previous lectures: focus on discrete-time setting
This lecture: focus on continuous-time setting
dynamic programming approach leads to HJB / HJI equation: non-linear partial differential equation
HJB application: solution to continuous LQR problem
HJI application: reachability analysis
Readings: lecture notes and references therein, in particular:
Bansal S., Chen M., Herbert S., Tomlin C. J., “Hamilton-Jacobi reachability: A brief overview and recent advances,” 2017.
Chen M., Tomlin C. J., “Hamilton–Jacobi reachability: Some recent theoretical advances and applications in unmanned airspace management,” 2018.

## Slide 4: Continuous-time model
Last time:
Model:
Cost:
This time:
Model:
Cost:
where and are fixed

## Slide 5: Two-person, zero-sum differential games
What if there is another player (e.g., nature) that interferes with the fulfillment of our objective?
Two-person differential game:
Model: (joint system dynamics),
Cost:
Player 1, with control will attempt to maximize , while Player 2, with control , will aim to minimize , subject to the joint system dynamics
is the joint system state
Notes: Useful to reason about diturbances

## Slide 6: Information pattern
To fully specify the game, we need to specify the information pattern
“Open-loop” strategies
  Player 1, with control declares entire plan
  Player 2, with control responds optimally
  Conservative, unrealistic, but computationally cheap
“Nonanticipative” strategies
  Other agent acts based on state and control trajectory up to current time
  Notation:
  Disturbance still has the advantage: it gets to (instantaneously) react to the control!
Notes: Reacts instantaneously, but does not know what we are doing in the future

## Slide 7: Hamilton-Jacobi-Isaacs (HJI) equation
Key idea: apply principle of optimality
The “truncated” problem is
Worst-case disturbance – aims to thwart the controller
Notes: Player 1 will attempt to maximize this outcome, while the Player 2 will aim to minimize it, subject to the system dynamics in (1).
Find u that makes cost as high as possible under most damaging disturbance
So instead of choosing an open-loop , the adversary chooses a policy that reacts to —but only causally.
In other words, The disturbance chooses a strategy anticipating the best response of the controller.
“For every disturbance strategy, the controller responds optimally.”
Then the disturbance picks the worst-case knowing that fact.
So:
disturbance is the outer minimizer
controller is the best-response maximizer
T_f = 0
J( \x(t), \uc(\tau)_{t\leq\tau\leq t_f}, t) = h(\x(t_f), t_f) + \int_{t}^{t_f}\, g(\x(\tau), \uc(\tau),\tau) \, d\tau
Player 1 will attempt to maximize this outcome, while the Player 2 will aim to minimize it, subject to the system dynamics in (1).
Find u that makes cost as high as possible under most damaging disturbance
So instead of choosing an open-loop 𝑤(𝑡), the adversary chooses a policy that reacts to 𝑢—but only causally.
In other words, The disturbance chooses a strategy anticipating the best response of the controller.
“For every disturbance strategy, the controller responds optimally.”
Then the disturbance picks the worst-case knowing that fact.
So:
disturbance is the outer minimizer
controller is the best-response maximizer
T_f = 0
J( \x(t), \uc(\tau)_{t\leq\tau\leq t_f}, t) = h(\x(t_f), t_f) + \int_{t}^{t_f}\, g(\x(\tau), \uc(\tau),\tau) \, d\tau

## Slide 8: HJI equation
Dynamic programming principle:
  Approximate integral and Taylor expand
  Derive Hamilton-Jacobi-Isaacs partial differential equation (HJI PDE)

## Slide 9: HJI equation
Approximations for small :

## Slide 10: HJI equation
Approximations for small :

## Slide 11: HJI equation
Approximations for small :

## Slide 12: HJI equation
Approximations for small :

## Slide 13: HJI equation
Approximations for small :
  Omit dependence…
  does not depend on or
Assume (instantaneously) constant and  optimization over vectors, not functions!
Order of max and min reverse (proof given in references)
Notes: So locally, the disturbance is optimizing given .
At the instantaneous scale:
the disturbance is not choosing a whole trajectory independently anymore
it is choosing a reaction to the current control
So the nested structure changes from:
“outer player picks a function anticipating optimal response”
to:
“at each instant, one player moves, then the other reacts”
That is exactly what swaps the order.
So locally, the disturbance is optimizing given 𝑢(𝑡).
At the instantaneous scale:
the disturbance is not choosing a whole trajectory independently anymore
it is choosing a reaction to the current control
So the nested structure changes from:
“outer player picks a function anticipating optimal response”
to:
“at each instant, one player moves, then the other reacts”
That is exactly what swaps the order.

## Slide 14: HJI equation
Approximations for small :
  Omit dependence…
  does not depend on or
Assume (instantaneously) constant and  optimization over vectors, not functions!
Order of max and min reverse (proof given in references)

## Slide 15: HJI equation
Approximations for small :
  Omit dependence…
  does not depend on or
Assume (instantaneously) constant and  optimization over vectors, not functions!
Order of max and min reverse (proof given in references)

## Slide 16: HJI equation
Approximations for small :
  Omit dependence…
  does not depend on or
Assume (instantaneously) constant and  optimization over vectors, not functions!
Order of max and min reverse (proof given in references)

## Slide 17: HJI equation
The end result is the Hamilton-Jacobi-Isaacs (HJI) equation
with boundary condition
Given the cost-to-go function, the optimal control for Player 1 is
The “Hamiltonian”
Notes: 0 = J^*_t(\x(t), t)+ \min_{\uc(t)} \biggl\{ g(\x(t), \uc(t),t) + J^*_{\x}(\x(t), t)^{\prime}\, \ad(\x(t), \uc(t), t) \biggr\}
J^*(\x(t_f), t_f) = h(\x(t_f), t_f)

## Slide 18: HJB equation
In case there is no disturbance, end result is the Hamilton-Jacobi-Bellman (HJB) equation
with boundary condition
Given the cost-to-go function, the optimal control is
Without a disturbance, is usually selected to minimize cost
Notes: rate of change of optimal value over time = best instantaneous gain under optimal control
Why minus? “moving forward in time reduces remaining cost-to-go”
Deeo connections with pmp
0 = J^*_t(\x(t), t)+ \min_{\uc(t)} \biggl\{ g(\x(t), \uc(t),t) + J^*_{\x}(\x(t), t)^{\prime}\, \ad(\x(t), \uc(t), t) \biggr\}
J^*(\x(t_f), t_f) = h(\x(t_f), t_f)

## Slide 19: Continuous-time LQR
Continuous-time LQR: select control inputs to minimize
subject to the dynamics
Assumptions:
and specified
and unconstrained
Notes: J(\x_0) = \frac{1}{2}\x(t_f)^T H \x(t_f) + \frac{1}{2}\int_{t_0}^{t_f}[\x(t)^TQ(t)\x(t) + \u(t)^TR(t)\u(t)]dt

## Slide 20: Continuous-time LQR
As before, value function takes the form:
The HJB equation reduces to an ODE (the Riccati equation):
Riccati equation is integrated backwards, with boundary condition
Once we find the control policy is
Analogously to the discrete case, under some additional assumptions, constant in the infinite horizon setting
See Notes §3.3 for more details
Notes: -\dot V(t) = Q(t) - V(t)B(t)R(t)^{-1}B(t)^TV(t) + V(t)A(t) + A(t)^TV(t)
\u^*(t) = -R(t)^{-1}B(t)^TV(t)\x(t)

## Slide 21: Applications of differential games
Pursuit-evasion games
  homicidal chauffeur problem
Reachability analysis
And many more (e.g., in economics)
Notes: The homicidal chauffeur problem is a pursuit–evasion differential game where a constrained vehicle tries to intercept a freely moving target, producing a nontrivial HJI equation whose solution encodes optimal interception geometry under curvature constraints. -> it’s not just distance—it’s geometry + curvature
More precisely:
If the evader is sufficiently far and laterally positioned,
it can always move in a direction that keeps the car “turning in place” instead of closing distance.
So there exists a region where:
the evader can maintain a persistent escape trajectory despite being slower or comparable in speed.

## Slide 22: Applications of differential games
Pursuit-evasion games
  homicidal chauffeur problem
Reachability analysis
And many more (e.g., in economics)

## Slide 23: Reachability analysis: avoidance
Inputs:
System model
Unsafe region: e.g., obstacle
Unsafe region
Backward reachable set
(States leading to danger)
Reachable set
Control policy
Notes: In reachability theory, we are often interested in computing the backward reachable set of a dynamical system.
This is the set of states such that the trajectories that start from this set can reach some given target set
If the target set consists of those states that are known to be unsafe, then the BRS contains states which are potentially unsafe and should therefore be avoided.

## Slide 24: Reachability analysis: goal reaching
Backward reachable set
Target set
Inputs:
System model
Goal region
Backward reachable set
(States leading to goal)
Control policy

## Slide 25: Reachability analysis
Model of robot
Unsafe region
Backward reachable set (states leading to danger)
Control policy
Model of robot
Goal region
Backward reachable set (states leading to goal)
Control policy

## Slide 26: Reachability analysis
Model of robot
Unsafe region
Backward reachable set (states leading to danger)
Control policy
Model of robot
Goal region
Backward reachable set (states leading to goal)
Control policy
States at time satisfying the following:
there exists a disturbance such that for all control, system enters target set at
26
States at time satisfying the following:
for all disturbances, there exists a control such that system enters target set at

## Slide 27: From HJI to reachability analysis
Computation of the BRS entails solving a differential game where the outcome is Boolean (the system either reaches the target set or not)
One can “encode” this Boolean outcome in the HJI PDE by (1) removing the running cost and (2) picking the final cost to denote set membership
  Value function at each state is the worst case terminal value you can reach

## Slide 28: From HJI to reachability analysis
Hamilton-Jacobi Equation
Remove running cost
Pick final cost such that
  Example: If , we can pick
R
Notes: In particular, one can always find a Lipschitz function h(x) such that T (the target set) is equal to the zero sublevel set of h, that is, x ∈ T ⇔ h(x) ≤ 0
This allows us to find the solution to a game of kind by posing an auxiliary game of degree whose solution encodes that of the original problem: this is, in essence, the level set approach.
Key idea: represent sets as level sets of a function

## Slide 29: Pick Final Cost
Why is this correct?
  Final state is in if and only if
  To avoid , control should maximize
    Worst-case disturbance would minimize
,
target set

## Slide 30: Reaching vs. Avoiding
Avoiding danger
  BRS definition
  Value function
  HJI
  Optimal control
Reaching a goal
  BRS definition
  Value function
  HJI
  Optimal control

## Slide 31: “Sets” vs. “Tubes”
Backward reachable set (BRS)
  Only final time matters
  Initial states that pass through target are not necessarily in BRS
  Not ideal for safety
Backward reachable tube (BRT)
  Keep track of entire time duration
  Initial states that pass through target are in BRT
  Used to make safety guarantees
,
target set
Notes: it is reachability at any time within an interval

## Slide 32: “Sets” vs. “Tubes”
Backward reachable set (BRS)
Backward reachable tube (BRT)
,
target set
  Value function definition
  Value function obtained from
  Value function definition
  Value function obtained from

## Slide 33: Example: pursuit/evasion with two identical vehicles
With evader (a), pursuer (b) dynamics we consider the relative system in (a)’s frame
Courtesy of Ian Mitchell, “ToolboxLS”,
Section 2.6.1
Notes: Draw only the isosurface where the function value equals 0.”
\begin{bmatrix}\dot x_a \\ \dot y_a \\ \dot \theta_a\end{bmatrix} = \begin{bmatrix} v \cos(\theta_a) \\ v \sin(\theta_a) \\ u_a \end{bmatrix}, \quad \begin{bmatrix}\dot x_b \\ \dot y_b \\ \dot \theta_b\end{bmatrix} = \begin{bmatrix} v \cos(\theta_b) \\ v \sin(\theta_b) \\ u_b \end{bmatrix},\quad
u_a, u_b \in [-u_\text{max}, u_\text{max}]
\begin{bmatrix} \dot x_1 \\ \dot x_2 \\ \dot x_3 \end{bmatrix} = \begin{bmatrix} -v + v\cos(x_3) + u_a x_2 \\ v \sin(x_3) - u_a x_1 \\ u_b - u_a\end{bmatrix}

## Slide 34: Computational aspects
Computational complexity (traditional PDE solver)
  is computed on an -dimensional grid
  is reasonable; larger requires some compromises
  Dimensionality reduction methods (decoupling) sometimes help
Alternatives/related approaches
  Sacrifice global optimality
  Give up guarantees
  NN-based PDE solvers
  Sampling-based methods
  Reinforcement learning

## Slide 35: Next time
Model Predictive Control